## Slide 1: System Flow
Truth model,
a particular realization of the uncertainty space
Knowledge errors, measurement noise
Navigation system model
Estimation
(aero filters, EKF, observers)
Nominal model,
typically mean of each uncertainty is used
Prediction model
(if needed, not all guidance predicts future states)
Guidance algorithm

## Slide 2: Modeling
True State
Estimation
Estimated State
Guidance algorithm
Measurement Noise
Propagation
Process Noise
Notes: The full state vector is propagated inertially using IMU data
Accelerations are measured (with measurement errors) in body axes then converted (with orientation errors) into wind axes as lift and drag

## Slide 3: Variance Minimization
Consider first the linear case, with unconstrained control
For suitable choice of norm on the final covariance matrix, the problem reduces to a standard LQR with a particular boundary condition
  The required norm is the trace operator
  The LQ state weight matrix Q = I
The trace is a suitable choice in many cases. Geometrically, it is related to the size of the covariance ellipse, while ignoring directional information
In particular, it is similar to the L1 norm of the vector of eigenvalues

## Slide 4: Trace Norm
From the broader class of Schatten p-norms with p=1
Also called the nuclear norm, equal to the sum of the singular values (= eigenvalues because covariance is positive semi-definite)

## Slide 5: Variance Minimization
Next consider the same scenario with bounded control inputs
  The optimal control law is bang-bang in nature
  Can no longer decouple mean and covariance problems
In zero mean case, optimal control in linear feedback is achieved as K -> inf, resulting in bang-bang control = Umax*sign(x)
Even for linear problems, we turn to an optimization approach: find the optimal mean trajectory such that covariance is minimized under discontinuous feedback

## Slide 6
Reachable Set
Constraint, c(x) = 0
Initial Set
F(x)
Subset with probability P
Idea: Use reachable set to turn probabilistic constraint into deterministic
Given: an initial set and a constraint to be satisfied with probability P
Take a subset of the initial set that has probability P (this is not unique unless P=1)
Map the subset through the function F
If the subset does not violate the constraints, then the probabilistic constraint is satisfied
Acceptable constraint violation
This subset satisfies c(x) < 0 with probability at least P
Chance Constraints
Notes: The more states involved in the constraint, the more checks we have to perform. For a 1-D constraint, we only have to check a line’s worth of points. However, we don’t need to check constraints for every possible x and every possible y, we only need to check for points (x,y) that are in the reachable set.
A little more work, and we can also simply check points that are extremal, but this requires determining which points are extremals.
Many common approaches introduce conservatism, for example by using probabilistic inequalities based on moments (which are not tight in general). This approach has zero conservatism when F is invertible. If F is not, then some conservatism is introduced but likely still much smaller than