## Slide 1: A Stochastic Optimal Control Approach to Mars EDL
Connor Noyes
December 5th, 2018

## Slide 2: Outline
EDL Overview
EG Review
Stochastic Review

## Slide 3: Outline
Entry phase (hybrid opt, convex updating)
SRP phase (robust solutions via optimal control)
Multi-phase optimal control (create reference for initialization entry, and to track in SRP phase potentially)
Adaptive SRP initiation via free initial condition OCP?
Free final time via free initial condition?
Non-standard control objectives: risk sensitive, minimally covariant trajectories

## Slide 4: Entry, Descent, and Landing State of the Art
Mars Science Laboratory - Apollo entry guidance, DGB Chute, Sky-Crane Descent stage
Reference trajectory designed for slow maneuvers and wide margins
Closed-loop performance evaluated via Monte Carlo
  Iteration with human in the loop
Parachute architectures simply do not scale to high ballistic coefficients

## Slide 5: EDL Concept of Operations
Entry phase – vehicle is guided by orienting the lift vector, controlled by reaction control thrusters
Powered descent phase – supersonic retropropulsion is used to null nearly all of the vehicle’s remaining velocity
Landing phase – vertical powered descent phase to soft touchdown

## Slide 6: Features of the Entry Phase
Expressed in spherical coordinates
  State dimension = 6
  Underactuated with only one control
Exponential model of atmospheric density coupled with nonlinear aerodynamic forces result in a wide operating range
  Linear static feedback is insufficient; gain scheduling or nonlinear control is required for high performance

## Slide 7: Features of the Descent Phase
Dynamics comprise three double integrators (+ affine gravity term in vertical direction), and nonlinear mass dynamics
  State dimension = 7
The vehicle’s thrust is subject to nonlinear, non-convex constraints that couple the coordinate directions

## Slide 8: Overview of how our approach is different
Stochastic view of the problem; looking an entire tube of trajectories from the start
Reversal of order; reference trajectory is designed in view of closed-loop performance
  The process may still require iteration if the chosen controller parameters are insufficient
  In NLP formulations gains and other controller parameters can be included in the optimization

## Slide 9: Broadly…
I am interested in closed loop performance of constrained, nonlinear systems subject to parametric uncertainty and/or stochasticity
I want to exploit knowledge of the probabilistic nature of the uncertainty to improve performance

## Slide 10: Entry Guidance Literature
Drag tracking
Neighboring optimal control
Predictor-corrector

## Slide 11: Literature Review
Linear Exponential Gaussian (weights higher moments)
Control of Liouville equation
Desensitized optimal control penalizes the partial derivatives of the objective function wrt parameters, or places constraints on sensitivities
Mean-Variance trades off mean performance and robustness
  Decreasing the sensitivity of open-loop optimal solutions in decision making under uncertainty

## Slide 12: Literature Review
Optimal Trajectory Generation with Probabilistic System Uncertainty Using Polynomial Chaos (Fisher, Bhattacharya)
  Derived expressions for minimum expectation and minimum variance objectives in terms of PCE coefficients
  Considered open loop
Stochastic Trajectory Optimization for Mechanical Systems with Parametric Uncertainties
  Extended Differential Dynamic Programming to stochastic systems using polynomial chaos

## Slide 13: Also Related
Tube-based formulations (MPC), invariant sets
PDF shaping

## Slide 14: Existing Applications to EDL
Desensitized entry and powered descent without explicit enforcement of constraints
Variance penalization without confirmation of benefits

## Slide 15: Drawbacks/Limitations of Existing Approaches
Desensitized control does not make use of statistical information
  Indeed, performance evaluations are conducted using parameters governed by distributions and we can use this information explicitly
Few papers discuss closed-loop approaches
  Those that do avoid the issue of control constraints and instead impose arbitrary limits on the feedback gains or exclude feedback gains from the optimization process entirely
Generally only demonstrated on 2d examples, many proposed solutions do not scale well with increasing dimension
PCE only display spectral convergence for smooth systems
  Saturation nonlinearity slows convergence as a result

## Slide 16: Switch Time Optimization for Rapid Entry Trajectory Design
Simple parameterization for robust, near-optimal altitude performance intended for parachute architectures
Can show that this parameterization also allows for near-optimal minimum velocity performance, suitable for SRP applications
If-then logic used is discontinuous; Nelder-Mead simplex method has been used for optimization
Results from hybrid OC literature suggest a gradient based solution is possible and preferable

## Slide 17: Switch Time Opt
Gradients with respect to switch times cannot be easily evaluated via finite difference, and automatic differentiation fails due to the discontinuous logic
Solved very efficient via SQP method (quasiNewton method, BFGS update to inverse Hessian)
We left margins heuristically, assumed a fixed % was sufficient for closed loop trajectories

## Slide 18: Chance Constrained Nonlinear Optimal Control
(Covariance minimization is just one particular objective)
For Gaussian uncertainty, we cannot guarantee that constraints will be met due to unboundedness, instead they must be met with a specified probability

## Slide 19
YP
Reachable Set, Y
Constraint boundary, c(y) = 0
Initial Set, X
F(x)
Subset XP with probability P
Idea: Use reachable set to turn probabilistic constraint into deterministic constraints
Given: an initial uncertainty set (possibly unbounded) and a constraint to be satisfied with probability P
Take a subset of the initial set that has probability P (this is not unique unless P=1)
Map the subset through the function F
If the mapped subset does not violate the constraints, then the probabilistic constraint is satisfied, i.e.
Acceptable constraint violation
This subset satisfies c(y) < 0 with probability at least P
Chance Constraints
If F(x) is injective, the constraint is satisfied with probability P, i.e., no conservatism is introduced
Let
Then,
Two problems:
How to compute the reachable set efficiently?
How to impose constraints on the entire set?
Notes: The more states involved in the constraint, the more checks we have to perform. For a 1-D constraint, we only have to check a line’s worth of points. However, we don’t need to check constraints for every possible x and every possible y, we only need to check for points (x,y) that are in the reachable set.
A little more work, and we can also simply check points that are extremal, but this requires determining which points are extremals.
Many common approaches introduce conservatism, for example by using probabilistic inequalities based on moments (which are not tight in general). This approach has zero conservatism when F is invertible. If F is not, then some conservatism is introduced but likely still much smaller than

## Slide 20: Current Approach
Original Problem
Constraint Reformulation
Finite Constraint Relaxation
Reachable set is approximated by an ellipse around nominal trajectory based on the state covariance
Constraints are imposed on a finite number of points on the boundary of the ellipse, computed from the columns of the square root of the covariance matrix
The boundary of the ellipse under consideration is decided by the level of constraint satisfaction

## Slide 21: Drawbacks/Limitations
Use of linearized covariance propagation limits the size of ellipse under consideration
  Due to large uncertainty or stringent constraint satisfaction
  Strong nonlinearity or large ellipse will not accurately capture the state distribution, and the probabilistic bounds are not guaranteed to be satisfied
Assumption of linear feedback control
  Naturally there may exist nonlinear controllers that outperform linear feedback
Solution: Unscented transform scales as linear covariance propagation (when symmetry is not exploited)
  Relies on sampled trajectories which allows arbitrary dynamics and controller structure
Notes: The finite size of the ellipse provides a very natural scaling for the sigma points, i.e. we choose the initial set of sigma points to be on the boundary of the initial ellipse
Can deal with parametric uncertainty in the same framework. Linear cov prop can deal with stochastic dynamics, how can we do that with sigma points?
Answer: the total covariance is the state covariance P and the stochastic covariance Q along the diagonal [P 0; 0 Q]. Thus, any channel in which the noise acts increased the number of sigma points by 2

## Slide 22: Roadmap
Application to SRP with LQR controller
  Potential for improving NLP solution methodology via sequential convex programming; UT grows problem size but for specified gains, the problem remains convex
Extension to output feedback scenario with application to entry phase coupled with Apollo guidance, where the feedback states are measured or estimated quantities

## Slide 23: Covariance Minimization
Consider first the LTV case, with unconstrained control
For suitable choice of norm on the final covariance matrix, the problem reduces to standard LQR with a particular boundary condition
  The required norm is the trace operator
  The LQ state weight matrix Q = I
The trace is a suitable choice in many cases
  Geometrically, it is related to the size of the covariance ellipse, while ignoring directional information

## Slide 24: Variance Minimization
Next consider the same scenario with bounded control inputs
  The optimal control law is bang-bang in nature
  Can no longer decouple mean and covariance problems
In zero mean case, optimal control in linear feedback is achieved as K -> inf, resulting in bang-bang control = -Umax*sign(x)
Even for linear problems, we turn to an optimization approach: find the optimal mean trajectory such that covariance is minimized under discontinuous feedback

## Slide 25: 1D Example:
Notes: Provides a systematic way to bias the reference away from the constraints
Fixed endpoint at the origin
Drag effect is contracting, allows even the open loop scenarios to reduce the variance

## Slide 26: Application: Supersonic Retropropulsion
During vehicle design, we seek to minimize propellant use under uncertainty during the powered descent phase
  J = -m(tf)
  This allows us to deliver the heaviest payload to the surface
The system is subject to bounded thrust magnitude, glide-slope constraint that prevents shallow flight

## Slide 27
Targeted Landing Site
Optimal SRP Ignition (Nominal Scenario)
Entry trajectory, steered by bank angle commands, executed by small
RCS thrusters
Atmospheric entry interface
Downrange
Crossrange
For the same optimal altitude, velocity, and flight path angle, any point on the red circle will produce an equivalent SRP trajectory so long as the heading points to the target
This is interesting because it means that unlike with parachute architectures which try hard to arrive near zero crossrange, there is no such restriction on SRP-based landings

## Slide 28: Introduction
Future Mars missions will have challenging requirements that necessitate closed-loop entry guidance
The ability to design a trajectory onboard increases autonomy and can be used in entry guidance
  Trajectory generation can be used in reference tracking methods, or as the basis for a numerical predictor-corrector method via frequent design
Generating an optimal trajectory onboard is difficult due to limited computing resources
Notes: Can either augment an existing approach, or form the basis for a new one
Need to balance computation requirements

## Slide 29: Entry Trajectory Updating
The vehicle enters the atmosphere with a trajectory designed that will deliver it to the target under nominal conditions
Under off-nominal conditions, the vehicle will deviate from the trajectory that was planned, sometimes even with the aid of closed-loop guidance
  Vehicle may arrive at the target under poor conditions (e.g. outside of parachute deployment conditions) or may violate important path constraints
Goal: use current estimated vehicle state and redesign a path to the target while satisfying constraints (e.g. parachute deploy conditions, path constraints)
Notes: Entry vehicle flies with an angle of attack to generate lift
Vehicle is steered toward the target via rotation of the vehicle about the velocity vector to orient the lift vector
Many potential applications, including updates to a reference trajectory in a tracking approach, and predictor-corrector-like method based on regular repeated updates

## Slide 30: Proposed Approach
Trajectory update is posed an optimal control problem
  Objective is to minimize distance to original trajectory while satisfying constraints
Use energy as independent variable
Convexify
  Treat bank angle as additional state, use bank rate as the control variable
  Linearize the equations of motion
  Unlike powered descent case, convexification is not lossless
Discretize (or transcribe) into second-order cone program
  Chebyshev pseudospectral method
Solve the resulting SOCP using efficient interior-point solver
Notes: Minimizing distance to original trajectory keeps the linearization as accurate as possible
Treating the bank rate as control allows us to limit it, as an added benefit
Normal approaches are iterative, ours solves only a single problem
Bank limit becomes a path constraint, rather than control constraint

## Slide 31: Convex Optimization
(Iterative) Convex optimization approaches to non-convex optimal control problems have exploded in interest due to efficient, polynomial time solvers and guaranteed global solution when the problem is feasible
A variety of aerospace problems have been solved including ascent trajectory design, powered descent trajectory design, interplanetary transfers, and entry
While these convex optimization guarantees solution of feasible sub-problems, not all methods have guaranteed convergence, and those that do typically require an unknown number of iterations
  The proposed approach does not involve multiple iterations

## Slide 32: Single Trajectory Demonstration
Updates occur at 30s interval, and ceases below 1000 m/s
4% less drag, 4% more lift, and perturbations to atmospheric density are applied
Mismatch between state predicted by update 2 (green) and actual state due to parametric uncertainty and off-nominal atmospheric conditions is corrected by the following updates
Notes: Corrections are fairly substantial even for relatively small perturbations

## Slide 33: Single Trajectory (Cont.)
The initial trajectory was optimized for high altitude
The updates retain aspects of the original trajectory, e.g., altitude performance remains excellent
Parachute deployment box
All trajectories end at the same energy level due to use of energy as independent variable

## Slide 34: Monte Carlo Simulation
Vehicle is nominally L/D = 0.24 with initial state subject to MSL-like dispersions
MarsGRAM is used for environment modeling
Uncertainty is added to lift and drag coefficients
  Gaussian with 3σ = 10%
Updates occurs at 10 second intervals and stops at 600 m/s
Bank angle limited to ±90°, and bank rate limited to 20°/s
200 samples chosen by Sobol’ sequence
Trajectories terminate when they reach the correct downrange distance
  Simple logic, but should expect variations in final altitude and velocity despite energy as independent variable
Notes: No tracking, flown open-loop between plans, NO ADD’L LATERAL CONTROL
Low discrepancy sampling

## Slide 35: MCS Results - Groundtrack
Excellent crossrange performance due to coupled update to longitudinal and lateral channels
Interestingly, a small number of samples even have an additional reversal
Notes: Note the difference in scale between the axes
Also, not all trajectories are plotted, too unclear otherwise (that’s why there are samples at +- 1km crossrange not seen in the plots

## Slide 36: MCS Results – Altitude/Velocity
Although some trajectories exit the parachute deployment conditions, all but three pass through the box
  Solved by considering triggering logic that explicitly accounts for parachute conditions

## Slide 37: MCS Results – Bank Profiles
Largest difference is in the timing of bank reversals
Bank angle (and trajectory in general) deviates from the original trajectory most at the end
  This is expected because the later portion of trajectory is updated the greatest number of times

## Slide 38: Conclusion
Despite the use of linearization requiring small, local updates, a convex approach to onboard trajectory redesign shows promise
Use of updating has a number of potential applications
If the target point is not reachable, the solution returned by the optimizer may be outside the region of validity of the linearized trajectory, or the optimization may return infeasible
  Safeguarding is required
  Consider the endpoint constraint as a penalty term in the objective

## Slide 39: Trace Norm
From the broader class of Schatten p-norms with p=1
Also called the nuclear norm, equal to the sum of the singular values (= eigenvalues because covariance is positive semi-definite)

## Slide 40: System Flow
Truth model,
a particular realization of the uncertainty space
Knowledge errors, measurement noise
Navigation system model
Estimation
(aero filters, EKF, observers)
Nominal model,
typically mean of each uncertainty is used
Prediction model
(if needed, not all guidance predicts future states)
Guidance algorithm

## Slide 41: Modeling
True State
Estimation
Estimated State
Guidance algorithm
Measurement Noise
Propagation
Process Noise
Notes: The full state vector is propagated inertially using IMU data
Accelerations are measured (with measurement errors) in body axes then converted (with orientation errors) into wind axes as lift and drag